eevidtron episode 001
Serial Peripheral Interface (SPI)

---
SPI Topology
Picture Source: http://en.wikipedia.org/wiki/File:SPI_three_slaves.svg
Author: Colin M.L. Burnett, License: GFDL

---
SPI Pins
Pin	Long Name	Description / Notes
SS	Slave Select (Chip Select)	Select Slave Device (low-active) / Indicate start of transfer (negative edge)
SCK	Serial Clock	Generated by Master / One pulse per transferred bit
MOSI	Master Out – Slave In	Generated by Master / Data is transferred MSB first
MISO	Master In – Slave Out	Generated by active Slave / Data is transferred MSB first

---
SPI Transfer
Picture Source: http://en.wikipedia.org/wiki/File:SPI_8-bit_circular_transfer.svg
Author: Colin M.L. Burnett, License: GFDL

---
SPI Facts
- There is no SPI standard.
- Usually SS is active low and a word has 8 bits.
- Usually SS is also needed in single-slave configurations.
- There are 4 different “flavors” of SPI, called “SPI Modes”.
- It's impossible to transfer a word in one direction without also transferring one in the other direction.

---
SPI Modes
SPI Mode	CPOL (Clock Polarity)	CPHA (Clock Phase)
0	0	0
1	0	1
2	1	0
3	1	1
CPOL=0
Clock idle state is low, Positive pulses for data transfer
CPOL=1
Clock idle state is high, Negative pulses for data transfer
CPHA=0
Data is sampled on leading clock edge, must be set up earlier
CPHA=1
Data is set up on leading clock edge and sampled on trailing clock edge

---
SPI Mode 0
CPOL=0
Clock idle state is low, Positive pulses for data transfer
CPHA=0
Data is sampled on leading clock edge, must be set up earlier

---
SPI Mode 1
CPOL=0
Clock idle state is low, Positive pulses for data transfer
CPHA=1
Data is set up on leading clock edge and sampled on trailing clock edge

---
SPI Mode 2
CPOL=1
Clock idle state is high, Negative pulses for data transfer
CPHA=0
Data is sampled on leading clock edge, must be set up earlier

---
SPI Mode 3
CPOL=1
Clock idle state is high, Negative pulses for data transfer
CPHA=1
Data is set up on leading clock edge and sampled on trailing clock edge

---
Arduino SPI Example
#include <SPI.h>
#define SPI_PIN_SS 10
#define SPI_PIN_MOSI 11
#define SPI_PIN_MISO 12
#define SPI_PIN_SCK 13
void setup()
{
  Serial.begin(9600);
  pinMode(SPI_PIN_SS, OUTPUT);
  digitalWrite(SPI_PIN_SS, HIGH);
  SPI.begin();
}
void loop()
{
  int serial_byte = Serial.read();
  int spi_mode = -1;
  byte miso_data;
  if (serial_byte == '0') spi_mode = SPI_MODE0;
  if (serial_byte == '1') spi_mode = SPI_MODE1;
  if (serial_byte == '2') spi_mode = SPI_MODE2;
  if (serial_byte == '3') spi_mode = SPI_MODE3;
  if (spi_mode != -1)
  {
    // step 1: configure SPI mode
    SPI.setDataMode(spi_mode);
    // step 2: assert slave select
    digitalWrite(SPI_PIN_SS, LOW);
    // step 3: perform SPI transfers
    miso_data = SPI.transfer(0xf0 + spi_mode);
    miso_data = SPI.transfer(miso_data);
    // step 4: deassert slave select
    digitalWrite(SPI_PIN_SS, HIGH);
  }
}

---
MagicShifter SPI Example
[ probing LED driver data on MagicShifter board ]

---
Links
- Wikipedia Article on SPI
  - http://en.wikipedia.org/wiki/Serial_Peripheral_Interface_Bus
- Arduino SPI Library
  - http://arduino.cc/en/Reference/SPI
- MagicShifter
  - http://magicshifter.net/